FILE NAME: GWS Station Records Metadata – Alyeska Remote Power ARP1 2007.01.12.doc

LAST UPDATED:  01/12/07 09:22

BY:  R. F. Paetzold

UMIAT AIRPORT RAWS UPGRADE

STATION METADATA RECORDS

Edited by Austin McHugh 24 September 2007

STATION

NAME:  Umiat Airport

STATION ID:  3150

PAKBUS ID:  50

LOCATION:  _Umiat Airfield_____

GPS (00/00/06):	   69° 22.159’ N

152° 08.280’ W

260 ft elevation

MAP DATUM: 	WGS84

INSTRUMENT:	Garmin GPS V placed on top of air temperature radiation shield (2.0 m).

DATALOGGER

TYPE: CR1000

SERIAL NUMBER:  10135  Located on bottom of datalogger; record before installation.

WIRING PANEL SERIAL NUMBER:  9880  Located on front of wiring panel.

OPERATING SYSTEM (O/S):  CR1000 OS 13

PROGRAM:  Umiat Airfield RAWS 2007-9-22.CR1  Name Format: Station_year_month_day

TIME STANDARD: Alaska Standard Time  Datalogger time.

PERSONAL

| STATION MANAGER: Phone: FAX: E-mail: Web Page Address: | Name Address Line 1 Address Line 2 GWS Fairbanks, Alaska 99775 USA (907) (907) e-mail http://www. web page address |
| --- | --- |
| PROJECT PERSONNEL: Phone: FAX: E-mail: | Austin McHugh GW Scientific P.O. Box 81538 Fairbanks, Alaska 99708 USA (360-441-2023 (866)238-7608 austin@gwscientific.com |  |  |
| PROJECT PERSONNEL: Phone: FAX: E-mail: |  |  |  |
| LOCAL / OTHER PERSONNEL : Phone : FAX : E-mail : |  |  |  |

INSTRUMENTATION

Summary:

| Quantity | Description | Comments |
| --- | --- | --- |
| 1 | Campbell CR1000 datalogger sn: 10135 | Installed 09/18/07. |
| 1 | Campbell CR1000 wiring panel sn: 9880 | Installed 09/18/07. |
| 1 | TX312 GOES xmitter sn:1570 | Installed 09/18/07. |
| 1 | Freewave FGR-115RC radio sn: 915-6747 | Installed 09/18/07. actually before this date. |
| 1 | Antenna cable length- 50’ | Installed 09/18/07. actually before this date. |
| 1 | Antenna make and model – Coaxial LMR-400 | Installed 09/18/07. actually before this date. |
| 4 | Sun Xtender PVX-1040T 100-AH battery | Installed 09/18/07. actually before this date. |
| 1 | Morningstar SunSaver10 charger/regulator sn: SS10-12V | Installed 09/18/07. actually before this date. |
| 1 | Make & Model solar panel sn: NA—see photos | Installed 09/18/07. actually before this date. |
| 1 | enclosure- not Campbell, metal enclosure | Installed 09/18/07. |
| 1 | Campbell CM10 3-m tower | Installed 09/18/07. |
| 1 | CS105 Barometric Pressure Sensor (Vaisala PTB101B) sn:Z0740021 | Installed 09/18/07. actually before this date |
| 1 | RM Young Model 05103 wind monitor – 67035, O#151374 | Installed 09/18/07. |
|  | 05103 cable length 30’ |  |
| 1 | HMP45C sn: B4010028 | Installed 09/18/07 2.0-m height in 12-plate gill radiation shield. |
|  | HMP45C cable length 230 ft |  |
| 1 | TE525 Tipping Bucket Rain Gage sn:34078-704 | Installed 09/18/07. |
|  | TE525 cable length:200 ft |  |
| 1 | YSI model 4433 thermistor air temperature sensor (3 sensors/unit) (measuring 2 of 3) Labled: 07105 | Installed 09/18/07. 2.0-m height in 6-plate gill radiation shield. |
|  | YSI air temp cable length: 230’ |  |
| 1 | YSI model 4433 thermistor soil surface temperature sensor (3 sensors/unit) (measuring 2 of 3) Labled: 07106 | Installed 09/18/07. |
|  | YSI soil surface temp cable length: 230’ |  |
| 1 | YSI model 4433 thermistor -6” soil temperature sensor (3 sensors/unit) (measuring 2 of 3) Labled: 07107 | Installed 09/18/07. |
|  | YSI -6” soil temp cable length: 230’ |  |
| 1 | SR50A sn:C4561 | Installed 09/18/07. |
|  | SR50A cable length: 230 ft |  |
| 1 | Solar panel voltage divider 10K:1K |  |
|  | Record all models and serial numbers | Installed, replaced, location, etc. NOTE format for replacement shows old and new sensor; see Vaisala HMP45C for example. |

NOTES:  Defective sensors, reasons for replacements, re-wiring, upgrades, etc.

STATION HISTORY

Month 09, 2007:  This station was converted from a CR10X to a CR1000.  A TX312 GOES transmitter was added.  Sensors also added was an SR50A to measure snow depth, three GWS YSI triple thermistors to measure air temperature, soil surface temperature, and soil temperature 12 inches below the surface.

Equipment left from the previous installation includes and HMP45C air temperature and relative humidity sensor, 05103 wind monitor, TE525WS tipping bucket rain gage,  CS105 barometer.  Also maintained is the Freewave FGR115RC radio.

AC power charges the batteries from camp power when it is on.

The tripod was set-up with meteorological sensors and cables ran to a data logger in a near-by building.  A data logger was mounted about 200’ away, inside the near-by building.  A Freewave FGR-115RC line-of-sight radio was mounted in the enclosure and connected to the datalogger.  Power is supplied by the near-by camp and a unknown watt solar panel mounted on the south side of the building the logger panel is located.  Four Concorde 100-AH batteries was placed in the building containing the data logger.  Air, soil surface, and soil at -6” temperature sensors were installed and connected to the CR1000 datalogger.  The air temperature sensor is an YSI thermistor, mounted in a Campbell 41303-5A 6-plate gill radiation shield and attached to the tripod at a height of 2.0 m.  An RM Young wind sensor was installed at a height of 45 ft on the cross-arm of the tower.  It was aligned to true north with the aid of a Brunton Pocket Transit corrected for the local magnetic declination.  Datalogger time was set to Alaska Standard Time.  Midnight is 0000.  The datalogger program: Program scan rate is 5 seconds.  Wiring diagrams were enclosed in plastic sleeves and taped to the inside of the enclosure door with black electrical tape.  Photos of the completed station were taken.  – The date is the date of the installation completion.  A description of the station is given as well as any problems encountered.

Month 09, 2007:  Station maintenance –

RADIO SETTINGS

List all radio settings here, along with any other relevant information.

A copy of the radio settings file from the Freewave radio would be great here.

DATA

DATA PROCESSING ALGORITHMS

TEMPERATURE °C

Steinhart & Hart equation used to convert YSI thermistor readings to °C.

T (°C) = (1/(a + b(D + c(D^3)) – 273.15

Where:	a = 0.0014654354

b = 0.0002386780

c = 0.0000001000

D = ln(1000*Rs)

Rs = thermistor resistance (k()

DATA STORAGE AND ACCESS

Where the data reside and how to access data should be here along with the name and contact information for the person responsible for the data.

QA/QC

All QA/QC procedures may be too much to enter here.  A summary with a link to where the complete QA/QC documentation resides may be appropriate.  The summary should document the basic rules for recognizing questionable and bad data and how they are flagged or deleted.

SITE CHARACTERISTICS

LANDSCAPE

SLOPE:  00 %

ASPECT:  E (00º)

ELEVATION:  80 m

LANDSCAPE POSITION:  Flat tundra

Also geomorphology features, etc

SOILS

CLASSIFICATION:  If known

ACTIVE LAYER THICKNESS:  15 cm

STONENESS:  None

VEGETATION

GROUND COVER:  tundra, tussak, low shrubs/woody plants nearby

CANOPY COVER:  No Canopy.

If possible, list plant species and relative abundance.

LAND USE

Near Umiat.  Caribou present.  Arctic fox

DATA NOTES

For Example: Data gap from 12/29/05 to 04/20/06 due to low battery.

COMMENTS

Permafrost is approximately 6” below soil surface.

NOTES FOR NEXT STATION VISIT

Standard maintenance.

APPENDIX A

Site Photos

APPENDIX B

Wiring Diagrams

APPENDIX C

Current Datalogger Program

Umiat Airfield RAWS 2007-9-22.CR1

'Umiat Airfield RAWS 2007-09-22.cr

' Program modified: Umiat Airfield RAWS 2007-09-20.cr1

' Modified By: Austin McHugh

' Modifications: changed Daily table to get max of wind speed in m/s not mph

' Program modified: Umiat Airfield RAWS 2007-09-19.cr1

' Modified By: Austin McHugh

' Modifications:  Changed soil temps from xxx to xxx.x, added a daily table, added WSpd_ms and changed the label of the Daily

' wind vector to WindSpeedAvg_ms.  added WindSpeedAvg_ms to the end of the Atmospherics table.

' Program modified: Umiat Airfield RAWS 2007-09-18.cr1

' Modified By: Austin McHugh

' Modifications: Deleted several of the update comments below to make program shorter. Changed GOES WD to hourly from 10 minutes.

' Deleted SlrMj. Changed xmitted GOES precip to accumulated from hourly. Changed HMP45C to Sample from Average.  Changed 12inch soil to 6inch soil.

' Program modified: Umiat Airfield RAWS 2007-09-17.cr1

' Modified By: Austin McHugh

' Modifications: Corrected spelling of HourlyAtmospherics table.  Corrected error reading the rain gage was on C6, now P2.

' measure BP Not corrected every 1 minute.

' Program modified: Umiat Airfield RAWS 2007-09-14.cr1

' Modified By: Austin McHugh

' Modifications: Added code to compute YSI Air Temp in F.  Swapped to send the GWS YSI Air Temperature in F with the GOES 7 values and HMP45C temp in F in the upper.

''----------------------------------------------------------------------------------------------------------------------------------------------------

' GOES Data Output                                      Format                  Units

' 01    Rain cumulative total                           XX.XX     inches

' 02    WS 10 min avg                                   XXX       mph

' 03    WD 10 min avg                                   XXX       degrees

' 04    GWS YSI Air Temperature F sample                XXX       F

' 05    Fuel Temp Sample                                XXX       F  (set to 0)

' 06    RH 10 min avg                                   XXX       Percent

' 07    Battery Voltage Sample                          XX.X      Volts

' 08    Barometric Pressure  Sample                     XX.XX     In of Hg

' 09    Hourly Dir of Peak Wind                         XXX       Dir

' 10    Hourly Peak WS                                  XXX       mph

'	11	   Snow Depth Hourly "cleaned" average						XXX				cm

'	12	   Air Temp (HMP45C) sample				  	  					XXX				F

'	13	   GWS Soil Temperature Hourly average 						XXX.X			C

'	14	   GWS Soil Temperature at -6 average  						XXX.X 		C

'Note: Do NOT apply power to the TX312 until the antenna is connected

'Note: GOES can NOT transmit w/o a GPS fix.

'CRBasic angle units are in Radians by default.

AngleDegrees

Const SensorHt=195   'ENTER HEIGHT OF SNOW DEPTH SENSOR ABOVE GROUND 195 (cm) HERE <-----

'  For YSI thermistors -- conversion of kOHM to deg C

Const a = 0.0014654354

Const b = 0.0002386780

Const c = 0.0000001000

Dim j

Dim D(12)

'Sensor Variables -------------------------------------------------------------------------------------------------------------------------------

Public Batt_Volt,  Panel_TempF, AirTempF, RH

Public SolarPnlV

Public Rain_in

Public BP_inHg_C, BP_mBar_NC ' C = Corrected to sea level, NC = Not Corrected to sea level

Public FuelT_F

Public BPElev_ft

Public Raintot

Public MaxWS, MaxWD

Public Panel_TempC, AirTempC, TdewC, TdewF

Public setup_rc, msg_window

Public StationID

Public WDir

Public WSpd_knots, Wspd_ms

Public WSpd_mph

Public SR50(2), TCDT, SR50_Bad, Snowdepth,

Alias SR50(1)=DT

Alias SR50(2)=SR50_quality

Public GWSAirTemp(2), GWSSoilTemp(2), GWSSoil6Temp(2)

Public GWSAirTempR(2), GWSSoilTempR(2), GWSSoil6TempR(2)

Public GWSAirTempF(2)

Public RC_Data, ClearError

Public SetupFlag

Public Status(13), location(6), time(7)

public i, TimeToXmit, PortState

Public CountDwn As Boolean, TwlvMinFlag As Boolean, TwoMinFlag As Boolean

public ClockGood as boolean, SetClock as boolean,  DataTrigger as boolean

Alias Location(1)=GPSdataRC

Alias Location(2)=GPSSeconds

Alias Location(3)=Latitude

Alias Location(4)=Longitude

Alias Location(5)=Elevation

Alias Location(6)=MagDec

Alias Time(1)=Year

Alias Time(2)=Month

Alias Time(3)=Days

Alias Time(4)=Hours

Alias Time(5)=Minutes

Alias Time(6)=Seconds

Alias Time(7)=MicroSeconds

Alias Status(1)=RC_Status

Alias Status(2)=ST_Bytes

Alias Status(3)=ST_Days

Alias Status(4)=ST_Hour

Alias Status(5)=ST_Minute

Alias Status(6)=ST_Second

Alias Status(7)=Rdm_Bytes

Alias Status(8)=Rdm_Hour

Alias Status(9)=Rdm_Minute

Alias Status(10)=Rdm_Second

Alias Status(11)=FailSafe

Alias Status(12)=ST_BattVolt

Alias Status(13)=Ave_GPS

Const LASTRECORD=1

Const ST_APPEND = 0

Const ST_OVERWRITE = 1

Const RAWS7 = 3

Const XXX_X = 4

Const XX_XX = 5

Const X_XXX = 6

Const XXX = 7

Const XXXXX = 8

Const High = True

Const Low = False

Const ScanInterval = 5

Const PlatformID = &H326B17F6   'NESDIS ID as 8 hex characters ' 326B17F6

Const MsgWindow = 10            'Message window in Seconds ' 10

Const STChannel = 158           'Self-Timed channel number ' 158

Const STBaud = 300              'Self-Timed Baud Rate ' 300

Const RChannel = 151            'Random Channel number, not = zero ' leave at 151

Const RBaud = 100               'Random Channel Baud Rate ' leave at 100

Const STinterval = "00_01_00_00" 'Self-Timed interval:"day_hour_minute_second", as string ' as hourly

Const STOffset = "00_23_50"      'Self-Timed offset:"Hour_Minute_Second" ' as "00_23_50"

Const RInterval = "00_30_00"     'Random Interval:"Hour_minute_second" ' leave as is

'-------------------------------------------------------------------------------

Units WSpd_mph=miles/hour

Units WSpd_ms=m/s

Units WDir=Degrees

Units Batt_Volt=Volts

Units SolarPnlV=Volts

Units AirTempF=Deg F

Units RH=%

Units BPElev_Ft=feet

Units Rain_in=inch

Units Raintot=inch

Units FuelT_F=Deg F

Units AirTempC=Deg C

Units TdewF=Deg F

Units TdewC = Deg C

Units Panel_TempC=Deg C

Units Panel_TempF = Deg F

Units WSpd_knots=knots

Units SnowDepth=cm

Units GWSAirTemp(2)=DegC

Units GWSSoilTemp(2)=DegC

Units GWSSoil6Temp(2)=DegC

Units GWSAirTempF(2)=DegF

DataTable(RAWS,TwoMinFlag,100)        ' RAWS7 data table ---------------------------------------------------------------------

Sample (1,Raintot,fp2)

WindVector (1,WSpd_mph,WDir,FP2,False,0,0,1)

Sample (1,GWSAirTempF(1),FP2)   ' <<<<<<<<<<<<<<<<< we are using the GWS YSI thermistor in DegF for the RAWS air temperature sensor

Sample (1,FuelT_F,FP2)

Average (1,RH,FP2,False)

Sample (1,Batt_Volt,FP2)

EndTable

DataTable(RawsXd8,TwoMinFlag,100)       ' Sample BP xx.xx

Sample(1,BP_inHg_C,fp2)

EndTable

DataTable (RawsXd9,TwoMinFlag,100)      ' Dir of Peak WS: XXX

Sample(1,MaxWD,fp2)

EndTable

DataTable (RawsXd10,TwoMinFlag,100)     ' Peak WS: XXX

Sample(1,MaxWS,fp2)

EndTable

DataTable (RawsXd11,TwoMinFlag,100)     ' Average Snow Depth: XXX

Average(1,Snowdepth, fp2,SR50_Bad)

EndTable

DataTable (RawsXd12,TwoMinFlag,100)     ' Average GWS Air Temp XXX

Sample (1,AirTempF,FP2)  '<<<<<<<<<<<<<< this is the HMP45C in F.

EndTable

DataTable (RawsXd13,TwoMinFlag,100)     ' Average GWS Soil Temp XXX

Average(1,GWSSoilTemp(1), fp2,false)

EndTable

DataTable (RawsXd14,TwoMinFlag,100)     ' Average GWS Soil at -12 Temp XXX

Average(1,GWSSoil6Temp(1), fp2,false)

EndTable

' Original 2-minute wind table

DataTable(TwoMinWind,true,-1)

DataInterval(0,2,Min,10)

Sample(1, STATIONID, FP2)

WindVector(1,WSpd_knots,WDir, FP2, 0, 0, 0, 0)

FieldNames("MeanWindSpeed:knots,VectorWindDir:deg,WindDirStdDev")

Maximum(1,WSpd_knots, FP2, 0, False)

EndTable

DataTable(Hourly_Data,true,-1)

DataInterval(0,60,Min,10)

Sample(1, STATIONID, FP2)

WindVector(1,WSpd_knots,WDir, FP2, 0, 0, 0, 0)

FieldNames("MeanWindSpeed:knots,VectorWindDir:deg,WindDirStdDev")

Maximum(1,WSpd_knots, FP2, 0, False)

Average(1,AirTempC, FP2, 0)

Average(1,TdewC, FP2, 0)

Minimum(1,AirTempC, FP2, 0, False)

Sample(1,BP_mBar_NC, FP2)

Totalize(1,Rain_in, FP2, 0)

EndTable

' a new table for new met sensors

DataTable(HourlyAtmospherics, true, -1)

DataInterval(0,60,Min,10)

Sample(1, STATIONID, FP2)

average(1,AirTempC,fp2,SR50_Bad)

maximum (1,AirTempC,FP2,False,False)

minimum (1,AirTempC,FP2,False,False)

Sample(1,RH, FP2)

Maximum(1,RH, FP2, 0, False)

Minimum(1,RH, FP2, 0, False)

Average(2,GWSAirTemp(),FP2,False)

Average(1,snowdepth,fp2,SR50_Bad)' this is a "cleaned" value

maximum (1,snowdepth,FP2,False,False)

Minimum (1,snowdepth,FP2,False,False)

sample (1,snowdepth,FP2)

Sample (1,SR50_quality,FP2)

WindVector (1,Wspd_ms,WDir,FP2,False,0,0,0)

FieldNames("WindSpeedAvg_ms:ms,VectorWindDir:deg,WindDirStdDev")

EndTable

' a new table for sub surface measurements

DataTable(HourlySubSurface, true, -1)

DataInterval(0,60,Min,10)

Sample(1, STATIONID, FP2)

Average(2,GWSSoilTemp(),FP2,False)

Average(2,GWSSoil6Temp(),FP2,False)

EndTable

DataTable(HourlyRaw, true, -1)

DataInterval(0,60,Min,10)

Sample(1, STATIONID, FP2)

Average (2,GWSAirTempR(),FP2,False)

Average (2,GWSSoilTempR(),FP2,False)

Average (2,GWSSoil6TempR(),FP2,False)

EndTable

DataTable(HourlyDiag, true, -1)

DataInterval(0,60,Min,10)

Sample(1, STATIONID, FP2)

Average(1,Batt_Volt, FP2,False)

Average(1,Panel_TempC, FP2, False)

Average (1,SolarPnlV,FP2,False)

EndTable

DataTable (Daily, 1,-1)

DataInterval(0,1440,Min,0)

Sample(1,StationID,fp2)

Average (1,AirTempC,FP2,False)

Maximum (1,AirTempC,FP2,False,False)

Minimum (1,AirTempC,FP2,False,False)

Average (2,GWSAirTemp(),FP2,False)

Maximum (2,GWSAirTemp(),FP2,False,False)

Minimum (2,GWSAirTemp(),FP2,False,False)

Average (2,GWSSoilTemp(),FP2,False)

Maximum (2,GWSSoilTemp(),FP2,False,False)

Minimum (2,GWSSoilTemp(),FP2,False,False)

Average (2,GWSSoil6Temp(),FP2,False)

Maximum (2,GWSSoil6Temp(),FP2,False,False)

Minimum (2,GWSSoil6Temp(),FP2,False,False)

Maximum (1,RH,FP2,False,False)

Minimum (1,RH,FP2,False,False)

WindVector (1,Wspd_ms,WDir,FP2,False,0,0,0)

FieldNames("WindSpeedAvg_ms:ms,VectorWindDir:deg,WindDirStdDev")

Maximum (1,Wspd_ms,FP2,False,False)

Totalize (1,Rain_in,FP2,False)

Average(1,snowdepth,fp2,SR50_Bad)  ' this is a "cleaned" value

EndTable

' **************** Subroutine Setupsub ************************

sub setupsub                            'Uses Constants for GoesSetup(), June 18, 2007

goessetup(SEtup_RC,PlatformID,MsgWindow,STChannel,STBaud,RChannel,RBaud,STInterval,STOffset,RInterval)

endsub

' ********************** TimeSet ****************************************

sub TimeSet               'Set CR1000 clock to GMT time via TX312

if  SetClock then

GOESGPS(Location(),time())

' convert elevation in cm to BPelev_ft in feet once after it is optained from TX312, added AMcHugh

BPelev_ft = (elevation/100) * 3.281

if GPSdataRC < 1 then

if Hours>=0and Hours<24and Minutes>=0and Minutes<60and Seconds>=0and Seconds<60 then

'	ClockSet (Time())  'ClockSet is dissabled AMcHugh  The datalogger clock is not used to transmit data.

ClockGood = true

SetClock = false

endif

endif

EndIf

EndSub

' **************** subroutine Stats *************************

Sub Stats

GOESStatus (Status(),1)

endsub

'***************** Subroutine CountDown ***********************

sub CountDown

If ClockGood then

If not CountDwn then

If ST_Hour < 1 and St_Minute < 59 and ST_Minute > 15 then

TimeToXmit = (ST_Minute * 60) + ST_Second

Countdwn = true

endif

EndIf

endif

endsub

'*****************Subroutine Counting ************************

Sub Counting

if ClockGood then

if countDwn then

TimeToXmit = TimeToXmit - ScanInterval          ' june 18, 2007

If TimeToXmit <= 720 Then TwlvMinFlag = True

If TimeToXmit <= 120 then

TwoMinFlag = True

CountDwn = false

EndIf

endif

endif

Endsub

'Main Program -----------------------------------------------------------------------------------------------------------------------------------

BeginProg

SetClock = True

ClockGood = False

CountDwn = False

setup_RC=1

msg_window=-1

MaxWS = -20000  'initialize Max ws and wd, june 18

MaxWD = 0

Scan (ScanInterval,Sec,0,0)     'Const ScanInterval in seconds june 18, 2007

if SEtup_RC > 0 then

call setupsub

endif

STATIONID = 3150

Battery(Batt_Volt)

PanelTemp(Panel_TempC,250)

Panel_TempF=Panel_TempC*1.8+32

VoltSe (SolarPnlV,1,mV2500,15,1,0,250,0.011,0)

'''''''''''''''''''''''''''''''''''

''                               ''

'' Measure HMP45C                ''

''                               ''

'''''''''''''''''''''''''''''''''''

' this sensor is currently wired to 12v and ON always.

PortSet(2, 1)

Delay(0,150,MSEC)

VoltSe(AirTempC, 1, mV2500, 3, False, 0, 250, 0.1, -40)

VoltSe(RH, 1, mV2500, 4, False, 0, 250, 0.1, 0)

PortSet(2, 0)

If RH>100 AND RH<108 Then RH=100

AirTempF=AirTempC*1.8+32

'''''''''''''''''''''''''''''''''''

''                               ''

'' Measure Wind Monitor          ''

''                               ''

'''''''''''''''''''''''''''''''''''

BrHalf(WDir, 1, mV2500, 2, VX1, 1, 2500, False, 20000, 250, 355, 0)

' 05103 uses a multiplier of 0.2192 to get mph

PulseCount(WSpd_mph, 1, 1, 1, 1, 0.2192, 0)

' 1mph = 0.869knots

WSpd_knots = WSpd_mph * 0.869

' 1 mile/hour (mph) = 0.447 meter/second

WSpd_ms = WSpd_mph * 0.447

If WSpd_mph > MaxWS Then          ' Track max Wind Speed and Dir, these are zeroed at two min flag.

MaxWS = WSpd_mph

MaxWD = WDir

EndIf

'''''''''''''''''''''''''''''''''''

''                               ''

'' Measure TE525WS               ''

''                               ''

'''''''''''''''''''''''''''''''''''

'TE525/TE525WS Rain Gauge measurement Rain_in 0.01"/tip:

PulseCount(Rain_in,1,2,2,0,0.01,0)

Raintot = Raintot + rain_in

'''''''''''''''''''''''''''''''''''

''                               ''

'' Measure GWSAirTemp Thermistors ''

''                               ''

'''''''''''''''''''''''''''''''''''

'     USE HALF BRIDGE TO MEASURE RATIO OF Vse TO Vex

'       FOR 2 YSI AIR TEMPERATURE THERMISTORS

BrHalf (GWSAirTempR(),2,mV2500,9,Vx2,2,2500,True,0,250,1,0)

'     CONVERT VOLTAGE RATIO TO RESISTANCE (kOHM) FOR 2 SENSORS

'     FIXED RESISTANCE = 1.0 kOHM

GWSAirTempR(1) = 1 * GWSAirTempR(1) / (1 - GWSAirTempR(1))

GWSAirTempR(2) = 1 * GWSAirTempR(2) / (1 - GWSAirTempR(2))

For j=1 To 2

D(j) = LN (1000*GWSAirTempR(j))                                 'ln resistance (ohm)

GWSAirTemp(j) = (1/(a + b*D(j) + c*(D(j))^3)) - 273.15     'Steinhart & Hart Equation

GWSAirTempF(j) = (GWSAirTemp(j)*1.8)+32  							' compute GWS Air Temperature in F

Next j

'''''''''''''''''''''''''''''''''''

''                               ''

'' Measure GWSSoilTemp Thermistors ''

''                               ''

'''''''''''''''''''''''''''''''''''

' first one on EX2

BrHalf (GWSSoilTempR(1),1,mV2500,11,Vx2,2,2500,True,0,250,1,0)

GWSSoilTempR(1) = 1 * GWSSoilTempR(1) / (1 - GWSSoilTempR(1))

D(1) = LN (1000*GWSSoilTempR(1))                                 'ln resistance (ohm)

GWSSoilTemp(1) = (1/(a + b*D(1) + c*(D(1))^3)) - 273.15     'Steinhart & Hart Equation

' second one on EX3

BrHalf (GWSSoilTempR(2),1,mV2500,12,Vx3,1,2500,True,0,250,1,0)

GWSSoilTempR(2) = 1 * GWSSoilTempR(2) / (1 - GWSSoilTempR(2))

D(2) = LN (1000*GWSSoilTempR(2))                                 'ln resistance (ohm)

GWSSoilTemp(2) = (1/(a + b*D(2) + c*(D(2))^3)) - 273.15     'Steinhart & Hart Equation

'''''''''''''''''''''''''''''''''''

''                               ''

'' Measure GWSSoil6Temp Thermistors ''

''                               ''

'''''''''''''''''''''''''''''''''''

' both on EX3

BrHalf (GWSSoil6TempR(),2,mV2500,13,Vx3,2,2500,True,0,250,1,0)

'     CONVERT VOLTAGE RATIO TO RESISTANCE (kOHM) FOR 2 SENSORS

'     FIXED RESISTANCE = 1.0 kOHM

GWSSoil6TempR(1) = 1 * GWSSoil6TempR(1) / (1 - GWSSoil6TempR(1))

GWSSoil6TempR(2) = 1 * GWSSoil6TempR(2) / (1 - GWSSoil6TempR(2))

For j=1 To 2

D(j) = LN (1000*GWSSoil6TempR(j))                                 'ln resistance (ohm)

GWSSoil6Temp(j) = (1/(a + b*D(j) + c*(D(j))^3)) - 273.15     'Steinhart & Hart Equation

Next j

''''''''''''''''''''''''''''''''''''

''                                ''

''  Measure Snow Depth and Not-Corrected BP every minute ''

''                                ''

''''''''''''''''''''''''''''''''''''

If IfTime(0,1,Min) Then

'SR50 Sonic Ranging Sensor (SDI-12 Output) measurements DT, TCDT, and DBTCDT:

SDI12Recorder(DT,3,0,"M1!",100.0,0)    'MEASURE DISTANCE TO SNOW (cm), changed to M1! to get the quaulity number too.

TCDT=DT*SQR((GWSAirTemp(1)+273.15)/273.15)  'CORRECT DISTANCE FOR AIR TEMPERATURE (cm)

Snowdepth=SensorHt-TCDT               'CALCULATE SNOW DEPTH (cm)

' create a variable to not process out-of-range snowdepth values

If Snowdepth < -25 OR Snowdepth > 100 Then SR50_Bad = 1 Else SR50_Bad = 0

' remove the multiplier from the quality number

SR50_quality=SR50_quality/100

' Turn on and read CS105 BP Not Corrected, then turn it off.

PortSet(1,1)    'turn on CS105

Delay(1,1000,mSec)      'pause after applying power

'measure CS105 (Vaisala PTB101) BP in mBar uncorrected. Multipler = 0.184 mBar/mv

VoltSe(BP_mBar_NC, 1, mV2500, 1,1, 0, 250, 0.184, 600)

PortSet(1,0)

EndIf

' set Fuel Temperature to 0 as a place holder per Richard Kemnitz request

FuelT_F = 0

'The equation used to calculate dew point is:

'Td=(241.88*ln(Vp/0.61078))/(17.558-ln(Vp/0.61078))

DewPoint(TdewC,AirTempC,RH)

If TdewC>AirTempC OR TdewC=NAN Then TdewC=AirTempC

TdewF=1.8*TdewC+32

'--- GOES Satellite code setup ----------------------------------------------------------------------------------------------------------

If msg_window Then              ' run when GOES setup parameters have been entered

'Time interval for read stats.

If IfTime(0,1,min) Then

If SetClock Then

Call timeset

EndIf

Call Stats

EndIf

Call CountDown

Call Counting

If TwoMinFlag Then 'Measure  BP

PortSet(1,1)    'turn on CS100

Delay(1,1000,mSec)      'pause after applying power

'measure CS105 (Vaisala PTB101) BP in mBar corrected. Multipler = 0.184 mBar/mv

VoltSe(BP_inHg_C,1,mV2500,1,1,0,250,0.184,600.0)  'measure Barometric sensor in mBar

BP_inHg_C=BP_inHg_C+(1013.25*(1-(1-((BPElev_Ft/3.281)/44307.69231))^5.25328)) ' compute offset in mBar

BP_inHg_C=BP_inHg_C*0.02953 'convert mBar to inHg

PortSet(1,0)

EndIf

' call the 10-minute outputs only when the 12-minute flag is high

If TwlvMinFlag Then

CallTable (RAWS)        ' Rain, WS, WD, AT, FT, RH, BV: RAWS7

CallTable (RawsXd8)     ' BP_inHg_C=In of Hg

EndIf

' call these tables every time because we want complete hourly averages.

' These must be called before the TwoMinFlag is set to 0.

CallTable (RawsXd9)     ' Sample Peak WD: XXX

CallTable (RawsXd10)    ' Sample Pead WS: XXX

CallTable (RawsXd11)     ' Average Snow Depth: XXX

CallTable (RawsXd12)     ' Sample GWS Air Temp XXX

CallTable (RawsXd13)     ' Average GWS Soil Temp XXX

CallTable (RawsXd14)     ' Average GWS Soil at -12 Temp XXX

If TwoMinFlag Then      'Shut down data taking until next hour

CountDwn = False

TwlvMinFlag = False

TwoMinFlag = False

MaxWS = 0

MaxWD = 0

'	raintot = 0  ' commmented out the 0 of raintot so that a cumulative precipitation would be transmitted.

GOESData(RC_data,RAWS,LASTRECORD,ST_OVERWRITE,RAWS7)

GOESData(RC_Data,RawsXd8,LASTRECORD,ST_APPEND,XX_XX)

GOESData(RC_data,RawsXd9,LASTRECORD,ST_APPEND,XXX)

GOESData(RC_data,RawsXd10,LASTRECORD,ST_APPEND,XXX)

GOESData(RC_data,RawsXd11,LASTRECORD,ST_APPEND,XXX)

GOESData(RC_data,RawsXd12,LASTRECORD,ST_APPEND,XXX)

GOESData(RC_data,RawsXd13,LASTRECORD,ST_APPEND,XXX_X) ' xxx.x

GOESData(RC_data,RawsXd14,LASTRECORD,ST_APPEND,XXX_X) ' xxx.x

EndIf

If IfTime(0,30,5) Then SetClock = True                 ' set the clock from GPS every 30 days

EndIf   ' end of GOES code

'Call Data Tables and Store Data --------------------------------------------

CallTable (TwoMinWind)

CallTable (Hourly_Data)

CallTable (HourlyAtmospherics)

CallTable (HourlySubSurface)

CallTable (HourlyRaw)

CallTable (HourlyDiag)

CallTable (Daily)

NextScan

EndProg